Triangle Scan-Conversion
# Pixel Coordinate System
Viewport on screen is specified in pixel coordinates
bounded in x by V_x0, ~V_x1
bounded in y by V_y0, ~V_y1
To map (x_p , y_p , z_p) form [-1,1] times [-1,1] times [0,1] into viewport (x_v , y_v , z_v) :
x_v `=` x_p {{V_x1 – V_x0} over 2} ~+~ {{V_x1 + V_x0} over 2}
y_v `=` y_p {{V_y1 – V_y0} over 2} ~+~ {{V_y1 + V_y0} over 2}
z_v `=` z_p
# Triangle
Determined by 3 points in floating point pixel coordinates.
P_0=(x_0, y_0, z_0), P_1=(x_1, y_1, z_1), P_2=(x_2, y_2, z_2)
Re-ordered so: y_0 <= y_1 <= y_2
# Edge equations scanline-to-scanline
Given a y scanline, calculate x and z
For edge from (x_i, y_i) to (x_j, y_j) :
x `=` m_xij y ~+~ b_xij newline z `=` m_zij y ~+~ b_zij
where
m_xij `=` {x_j – x_i} over {y_j –y_i}~~~ b_xij `=` {x_i y_j – x_j y_i} over {y_j – y_i} newline m_zij `=` {z_j – z_i} over {y_j –y_i}~~~ b_zij `=` {z_i y_j – z_j y_i} over {y_j – y_i} .
# Edge equations pixel-to-pixel
On a scanline y with endpoint (x_0 , y , z_0) and (x_1 , y , z_1) :
z `=` m_p x ~+~ b_p
where
m_p `=` {z_1 – z_0} over {x_1 –x_0}~~~ b_p `=` {z_0 x_1 – z_1 x_0} over {x_1 – x_0} .
# Outline
Split into two regions:
Region1: below the midpoint: y_0 <= y <= y_1
Region2: above the midpoint: y_1 <= y <= y_2

Rough algorithm:
For each scanline y in Region1:
x_S `=` ... ~~~ z_S `=` ... ~~~" using points " P_0, P_1 newline x_L `=` ... ~~~ z_L `=` ... ~~~" using points " P_0, P_2
For each pixel x in span x_S ... x_L :
Color pixel (x,y)
For each scanline y in Region2:
same as Region1 except use x_S ~=~ m_12 y + b_12

Many considerations:
Exactly which scanlines and which pixels?
Round or truncate?
Efficient calculations?
How to void double drawing of pixels?
Special cases? Like
y_0=y_1 or y_1=y_2 , or
x_S=x_L , or
y region has no scanlines, or
x span has no pixels.
# Exactly which pixels?
In order to avoid double drawing
(a) a triangle will fill in only pixels whose centers it contains
(b) but which triangle contains a pixel on the boundary?
Solution for (a):
careful use of floor and ceil
Solution for (b):
left/bottom filling rule,
and very careful use of floor and ceil
# Identifying pixels with centers contained
For a region y_0 <= y <= y_1
use scanline lceil y_0 rceil to lfloor y_1 rfloor , that is ceil(y_0) to floor(y_1) .
For a span of pixels on a scanline x_S ... x_L :
swap x_S ... x_L to ensure x_S<=x_L
use pixels lceil x_S rceil to lfloor x_L rfloor , that is ceil(x_S) to floor(x_L) .
This is almost what we want, except:
Problem: This can draw boundary pixels twice
if they fall on exact integer coordinates.
Next section solves that.
# The left/bottom fill rule
If two regions/spans meet exactly at an integer:
Let the upper one claim it.
Or equivalently
A triangle draws exact integers on left/bottom edges, but
does not draw exact integers on the other two directions.
Note behavior of floor and ceil
for exact integer y: floor(y) ~<>~ ceil(y-1)
for all other y: floor(y) ~=~ ceil(y-1)
which is exactly the behavior we want
So:
use pixels ceil(y_0) to ceil(y_1-1)
and similarly for pixels across a scanline
# Full Algorithm
ScanConvert( (x_0 , y_0 , z_0) , (x_1 , y_1 , z_1) , (x_2 , y_2 , z_2) )
Reorder points so y_0<=y_1<=y_2

if y_0 <> y_1	// Region 1
calculate slopes and intercepts m_x01 , b_x01 ~~ m_z01 , b_z01 ~~ m_x02 , b_x02 ~~ m_z02 , b_z02
for y from ceil(y_0) to ceil(y_1-1)
x_S `=` m_x01 y `+` b_x01 newline z_S `=` m_z01 y `+` b_z01 newline x_L `=` m_x02 y `+` b_x02 newline z_L `=` m_z02 y `+` b_z02
if x_S<x_L
x_0 , z_0 , ~~ x_1 , z_1 ~=~ x_S , z_S , ~~ x_L , z_L
else
x_0 , z_0 , ~~ x_1 , z_1 ~=~ x_L , z_L , ~~ x_S , z_S
calculate slope and intercept m_p , b_p from (x_0 , z_0) , ~~ (x_1 , z_1)
for x from ceil(x_0) to ceil(x_1-1)
z `=` m_p x `+` b_p
SetPixel (x,y,z)

if y_1 <> y_2	// Region 2
// Same except change 0 subscripts to 1 and 1 subscripts to 2.

# Notes:
Zbuffer is initialized:
to same size as cbuffer
all pixels get depth of 1.0 (since that is max possible depth)

Cbuffer is initialized
all pixels get background color

SetPixel(x,y,z):
  if zbuffer[x,y] > z:
    cbuffer[x,y] = Color at pixel (x,y,z) of object being rendered
    zbuffer[x,y] = z
# Efficiency
Loops in the algorithm calculate linear equations. For instance:
for y from y_first to y_last
x_S `=` m_x01 y `+` b_x01
A more efficient calculation can use an increment
x_S `=` m_x01 y_first `+` b_x01
for y from y_first to y_last
x_S `+{}=` m_x01