Phong Lighting Model
Section 4.3, pp 70-84
# Phong lighting components:
Emitted light: I_e ~=~ (I_e^R, I_e^G, I_e^B)
Diffuse: K_d ~=~ (K_d^R, K_d^G, K_d^B), ~~ K_a ~=~ (K_a^R, K_a^G, K_a^B)
Specular: K_s ~=~ (K_s^R, K_s^G, K_s^B) , n = shininess

Ambient light: I_a ~=~ (I_a^R, I_a^G, I_a^B)
Light i: I_i ~=~ (I_i^R, I_i^G, I_i^B)
Vectors, all normalized:
Vector towards light: L_i
Normal of surface: N
Direction toward eye: V
# Emitted
Light created by object and emitted equally in all directions
I_e ~=~ (I_e^R, I_e^G, I_e^B)
# Ambient
Light from all directions scattered equally in all directions
I_a K_a ~=~ (I_a^R, I_a^G, I_a^B)(K_a^R, K_a^G, K_a^B) ~=~ (I_a^R K_a^R, ~I_a^G K_a^G, ~I_a^B K_a^B)
# Diffuse
Light from a direction L_i scattered equally in all directions
I_i K_d cos %alpha ~=~ I_i K_d (N cdot L_i)
# Cosine falloff for diffuse
cos %theta ~=~ w/d so d ~=~ w/cos %theta
Amount of light in a beam of width w is Iw
Spread out over a length of d is
Iw over d ~=~ {Iw} over {w/cos %theta} ~=~ I cos %theta
# Specular
Light from the reflection direction R_i scattered equally in all directions
I_i K_s (cos %beta)^n ~=~ I_i K_s (V cdot R_i)^n

        cos^n(a) for n=powers of 2

# Computing R
Project L to Q to be perp to N:
alignl Q ~=~ L ~-~ {L cdot N} over {N cdot N} N ~=~ L - (L cdot N) N newline alignl R ~=~ L - 2Q newline alignl R ~=~ 2(L cdot N) N -L

# An alternative
Let H ~=~ (L+V)/left ldline L+V right rdline
Claim: b' = b/2
Proof: alignl 2 a ~+~ b ~=~ 2 a' newline alignl a' ~-~ b' ~=~ a newline alignl {} drarrow {b ~=~ 2 b' }
# Putting it all together
alignl I ~=~ I_e ~+~ I_a K_a ~+~ sum_i left(I_i K_d cos %alpha ~+~ I_i K_s cos %beta right) newline alignl I ~=~ I_e ~+~ I_a K_a ~+~ sum_i I_i left( K_d (N cdot L_i) ~+~ K_s (V cdot R_i)^n right)

once for each color of: I, I_e, I_a, K_d, L_i, K_s
# Coordinate systems
All calculations must be done in some consistent coordinate system
Will choose world coordinate system
Let V and P be the “viewing” and projection transformations respectively:	"world" {toward}^V~ "eye" {toward}^P~ "projection"
Transform things to world coordinates:
Normal: N is already in world coordinates
Position of lights: L is already in world coordinates
Eye position: (0,0,0) in eye CS becomes E `=` V^-1 (0,0,0,1)^T in world CS
Pixel object pos: (x,y,z,1) from scanline P `=` V^-1 P^-1 (x,y,z,1)^T (Then do hdiv)
# Distance attenuation
Light decreases with distance.
1/d^2 from a point source
1/d from an (infinite) linear source
constant from an (infinite) planar source
so use
f_a ~=~ 1 over {c_1 + c_2 d + c_3 d^2}
One set of reasonable values is
c_1 = c_2 = ¼, c_3 = ½
# Atmospheric attenuation (depth cuing, fog)
Blend calculated color I and fog color, I_fog
I' ~=~ s I ~+~ (1-s) I_fog
where s=1 for full color
and s=0 for full for fog
OpenGL implements three falloff functions for s:
LINEAR: {F-Z} over {F-N}
EXP: e^{-dZ}
EXP2: e^{-(dZ)^2}